## Slide 1: 24GHz ISM Multi-channel Radar Signal Chain Solution Complete RADAR Solution
Digital
Audio alert
AD8285 - 4 Ch (1)
ADAR7251 - 4 Ch (1)
PLL (1)
ADF4159/
ADF4158
Tx Chip (1)
ADF5901
Rx Chip (1)
ADF5904
ADSP-BF70 or
ADSP-2147x (DSP)
Best in class phase noise and high speed FMCW ramping for increased resolution
Digital signal processing solution included
EQ
ADC
AAF
EQ
ADC
AAF
EQ
ADC
AAF
EQ
ADC
AAF
Data Port
PLL FMCW Ramp Gen
DSP
MCU
M*
Transmit channel signal generation
Receive channel signal processing AFE
Transmit Antenna
Receive Antenna
© Analog Devices, Inc. 2016, all rights reserved.
Full signal chain solution
  Analog front end
  Mixed signal solution
  Digital baseband
Higher integration simplifies design and reduces time to market
Wider field of view with multiple channels
Separate Tx and Rx modules to provide flexibility in spatial design
Better noise and linearity resulting in greater effective range and accuracy
ADI Value
Multi channel architecture allows: beam forming for better field of view and angle resolution
Provides spatial flexibility
Simplifies design architecture with integration
ISM band allows worldwide application without restrictions
Architecture Benefits
ADF5904
24GHz, 4-channel Rx Downconverter
SPI programmable
Integrated temperature sensor
LO power detector
ADF5901
24GHz, 2-channel transmitter
8dBm power amplifier
-85dBc/Hz @ 100kHz VCO
-105dBc/Hz @ 1MHz VCO
ADF4159
0.5 – 13GHz Frac-N Synthesizer
25 bit divider modulus
110MHz PFD
AD8283
Analog baseband (AFE)
High speed ramps
12MHz input BW
12-bit, 80MSPS (all channels)
ADAR7251
Analog baseband (AFE)
Low speed ramps
1.2MHz input BW
16-bit, 2.4MSPS (per channel)

## Slide 2: Surveillance & Security Monitoring Motion detection and tracking of objects to optimize Surveillance & Security Systems
24GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLLs) with FMCW ramp generator
  ADAR7251/AD8284 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Multi channel system for digital beam forming:
  Wider field of view
  Best angular resolution
  Multi object or person detection & tracking
Higher receiver system SNR than current available solutions
  3dB better receiver noise figure
  Improved high performance transmitter phase noise, output power and high speed FMCW ramping
Technical Solution
More than x2 times improvement in sensitivity
More than x1.5 times better detection range
Much lower power consumption for small form outdoor use, with alternate and renewable power supply options
Key Benefits
Motion & Tracking Sensor
Notes: Data overload. Use movement to decide which video stream to focus on .

## Slide 3: DEMORAD - 24GHz Radar Sensor Platform Application Development on a Reference Design (SAP: EV-DEMORAD24G)
ADF5904 RX
ADF5901 TX
ADF4159 PLL
ADAR7251 AFE
ADSP-BF706
Single PC Board
Full ADI - Signal Chain - RF to Bits
4RX2TX (MIMO) Radar with BF-DSP digital baseband and Basic Radar software in GUI
Also Radar macros in DSP library

## Slide 4: DemoRad - Evaluation Demo Platform ( SAP: EV-DEMORAD24G)
ADF5904 RX
ADF5901 TX
ADF4159 PLL
ADAR7251 AFE
ADSP-BF706
Single PC Board
4RX2TX (MIMO) Radar + ADI-BF-DSP digital baseband + plus basic Radar software &GUI
Radar macros in DSP library
Full ADI - Signal Chain - RF to Bits
(USB Interface to PC)

## Slide 5: DemoRAD Block Diagram
Rx
ADF5904
Tx
ADF5901
AFE
ADAR7251
PLL
4159
DSP-
BF707
Control, Data Acquisition
Quad SPI
Python Script
PC
Target Identification & Visualization
USB
USB
SPI
2 TX Antennas
4 RX Antennas
DemoRAD

## Slide 6: Connecting the DemoRAD to MATLAB
DemoRAD connects to MATLAB & Phased Array System Toolbox
  Real-time beamforming and range doppler
  Platform to develop additional radar signal processing algorithms
Full model of DemoRAD (including antenna array) available to prototype new ideas in simulation
Range-Time Intensity
Angle-Time Intensity

## Slide 7: MATLAB
MATLAB scripts and ADI SW for DemoRAD can be downloaded from a FTP location (ftp://demorad_ftp:2H6cG78b@ftp.analog.com)
Folders of particular interest will be the ‘Python’ and ‘MATLAB’ folders.
This code is intended to serve as an example for further algorithm development.
The folders contain application notes showing how to access the data from DemoRad and pass it to MATLAB (or Python).
Data can be streamed from the DemoRAD into MATLAB, and there are example files on how to read it back to compute digital beam forming and range doppler.
The DemoRAD connects to MATLAB’s Phased Array System Toolbox.
The scripts implement the basic functions for configuring and operating the 24-GHz radar system. Therefore, it is the starting point to implement own applications.
The tutorials explain how to:
test USB connection from Matlab to the DSP board
read the software version of the board.
setup a connection to the DemoRad board
display the status information of the board in the command window of Matlab.
configure FMCW measurements, incl. RDM display.
read the antenna positions, access calibration data

## Slide 8: Features of the ADF 24-GHz FMCW Radar
DemoRad is a standalone radar system with a 24GHz MIMO FMCW frontend featuring two transmit (TX), four receive (RX) channels, ADC, and a Blackfin DSP from Analog Devices. The system is mainly designed for range-Doppler and MIMO radar applications and the DSP enables real-time signal processing capabilities. The antenna arrangement is chosen to support a uniform virtual array with a spacing of half the wavelength. When using both TX antennas 7 virtual elements can be generated with two virtual element overlapping in order to implement motion compensation algorithms. The main features of the 24GHz radar system include
  24GHz ISM band operation
  Sampling rate up to 1.2 MSPS per IF channel
  Ramp Synchronous sampling
  Freely programmable FMCW timing
  MIMO processing with arbitrary antenna activation
  Real-time signal processing on the Blackfin DSP
  USB 2.0 interface for communication.