## Slide 1
Emerging Applications
“Radar Sensor for the Emerging Masses”
ATS BU
(Autonomous Transportation & Safety)
Feb 2018
24GHz Radar Technology for
Broad Market Emerging Contactless Sensors
©2018 Analog Devices, Inc. All rights reserved.

## Slide 2: Agenda – introduction and evaluation of 24 GHz RADAR
Introduction to RADAR
Introduction to 24 GHz RADAR and applications
24 GHz RADAR chipset
24 GHz RADAR full system evaluation platform (DemoRAD)
Broad market RADAR use cases
24 GHz chipset product details
AFE/ADC product details
BF DSP Product details
Play introduction video

## Slide 3: This is Traditional “Radar” “RAdio Detection And Ranging”
©2018 Analog Devices, Inc. All rights reserved.
Very Old Principle: Sound Waves and Echo used to Judge distant (TOF) of large objects .. Cliffs or walls
RADAR based on same principle using RF:
RF signal and Echo/Reflections used to estimate distant / range of objects .. And with multiple Receivers .. Allows more reflections to be received returning at different angles thereby giving object angle information and therefore position with Doppler freq used to determine movement to/from TX

## Slide 4: This is new RADAR - Localized Sensing
Automotive Radar
ADAS Radar sensor
Intelligent Traffic Light Monitor Radar
Industrial Tank Level Radar
©2018 Analog Devices, Inc. All rights reserved.

## Slide 5: 24 GHz Industrial Broad Market Radar Three Major Industrial Application Segments
Many new opportunities emerging served by 24 GHz RF Radar Products that exist Today
Analog Devices offers many product solutions for 24 GHz radar sensors for emerging sensing applications
  Multi-Channel Radar for Object Detection & Tracking
    Smart Cities (Intelligent Traffic Monitoring & Control - Traffic flow & Infrastructure mgmt.)
    Surveillance & Security Monitoring
    Collision warning & avoidance – Boats/Train/UAV’s /Grounded Aircraft
  Radar for Precision Level Detection
    Industrial Proximity Measurement - Robotics
    UAV’s Altimeters
    Industrial Tank Level sensors
  Radar for Vital signs Monitor & Detection
    Vehicle Operators, Pilots, First Responders
    Elder care (aging-in-place)
    Room Occupancy (smart buildings)
Smarter World
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 6: Radar Frequencies & Sensor Performance comparisons
©2018 Analog Devices, Inc. All rights reserved.
Non-

## Slide 7: ITU World-Wide assigned ISM Band Frequencies 6 MHz to 250 GHz unlicensed spectrum:
mmw freq ISM bands
24 GHz is a WW available unlicensed ISM band
77 GHz/79 GHz is not an ISM band
  Restricted to Auto ADAS, Traffic Monitoring & Tank Level sensing applications only

## Slide 8: Analog Devices – Broad Market Radar group offers: 24 GHz Radar Full Signal Chain solution – Applicable to many emerging Industrial Sensing applications
RF Sub section
Mixed Signal Processing
Computer and Software
RF Antenna Element
RF, Microwave Group
Interface and Software Support
©2018 Analog Devices, Inc. All rights reserved.

## Slide 9
24 GHz RADAR chipset
and
24 GHz RADAR demo platform (DemoRAD)

## Slide 10: 24 GHz ISM Multi-channel Radar Signal Chain Solution Complete 24 GHz RADAR Solution - RF to Bits
Digital
Audio alert
AD8285 - 4 Ch (1)
ADAR7251 - 4 Ch (1)
PLL (1)
ADF4159/
ADF4158
Tx Chip (1)
ADF5901
Rx Chip (1)
ADF5904
ADSP-BF70 or
ADSP-2147x (DSP)
Best in class phase noise and high speed FMCW ramping for increased resolution
Digital signal processing solution included
EQ
ADC
AAF
EQ
ADC
AAF
EQ
ADC
AAF
EQ
ADC
AAF
Data Port
PLL FMCW Ramp Gen
DSP
MCU
M*
Transmit channel signal generation
Receive channel signal processing AFE
Transmit Antenna
Receive Antenna
© Analog Devices, Inc. 2018, all rights reserved.
Architecture Benefits and ADI Value
on next slide
ADF5904
24 GHz, 4-channel Rx Downconverter
SPI programmable
Integrated temperature sensor
LO power detector
ADF5901
24 GHz, 2-channel transmitter
8 dBm power amplifier
-85 dBc/Hz @ 100 kHz VCO
-105 dBc/Hz @ 1 MHz VCO
ADF4159
0.5 – 13 GHz Frac-N Synthesizer
25-bit divider modulus
110 MHz PFD
AD8283
Analog baseband (AFE)
High speed ramps
12 MHz input BW
12-bit, 80 MSPS (all channels)
ADAR7251
Analog baseband (AFE)
Low speed ramps
1.2 MHz input BW
16-bit, 2.4 MSPS (per channel)

## Slide 11: 24 GHz ISM Multi-channel Radar Signal Chain Solution Complete 24 GHz RADAR Solution - RF to Bits
© Analog Devices, Inc. 2018, all rights reserved.
Full signal chain solution
  Analog front end
  Mixed signal solution
  Digital baseband
Higher integration simplifies design and reduces time to market
Wider field of view with multiple channels
Separate Tx and Rx modules to provide flexibility in spatial design
Better noise and linearity resulting in greater effective range and accuracy
ADI Value
Multi channel architecture allows: beam forming for better field of view and angle resolution
Provides spatial flexibility
Simplifies design architecture with integration
ISM band allows worldwide application without restrictions
Architecture Benefits

## Slide 12: Analog Devices 24 GHz Radar Sensor Platform “DemoRAD” Application Development on a Reference Design
ADF5904 RX
ADF5901 TX
ADF4159 PLL
ADAR7251 AFE
ADSP-BF706
Single PC Board
4RX2TX (MIMO) Radar + ADI-BF-DSP digital baseband + plus basic Radar software & GUI
Radar macros in DSP library
Full ADI - Signal Chain - RF to Bits
(USB Interface to PC)
Plugs into Laptop using USB
Running Object Detection Mode
©2018 Analog Devices, Inc. All rights reserved.

## Slide 13: 24 GHz Radar Sensor Eval Platforms – Solution Application Development on a Reference Design
Rx
ADF5904
Tx
ADF5901
AFE
ADAR7251
PLL
4159
DSP-
BF706
Control, Data Acquisition
Quad SPI
Python Script
PC
Target Identification & Visualization
USB
USB
SPI
2 TX Antennas
4 RX Antennas
DemoRAD – Block Diagram
These solutions provide excellent aids to customers to achieve the following:-
  Low cost introduction to 24 GHz RF HW/SW sensor eval kit
  No need for expensive RF test & measurement equipment
  Quick and easy setup in minute to PC
  Understanding of RADAR HW and basic SW
  RF HW expertise and support
  Speeds up customer RADAR system evaluation
  Move quickly to reference design using “DemoRAD” platform
  Access to system partners or internal system experts
  Develop product with faster time to market
©2018 Analog Devices, Inc. All rights reserved.

## Slide 14: Demorad – Radar modes of operation Basic Radar Algorithms - Screen Shots
Range and velocity of target
Raw Data Capture
Radar sys data Range Data over time
Distance and angle of target
FMCW Mode
Range Doppler Mode
Digital Beam Forming Mode
©2018 Analog Devices, Inc. All rights reserved.

## Slide 15
24 GHz RADAR Broad Market Applications Examples
©2018 Analog Devices, Inc. All rights reserved.

## Slide 16: Use case: Intelligent Traffic Light Monitors Automating traffic light signals management to optimize the flow of traffic
24 GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLLs) with FMCW ramp generator
  ADAR7251/AD8285 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Multi channel system for digital beam forming:
  Wider field of view
  Best angular resolution
  Multi vehicle and person detection
Higher receiver system SNR than current available solutions
  3 dB better receiver noise figure
  Improved high performance transmitter phase noise, output power and high speed FMCW ramping
Technical Solution
More than ×2 times improvement in sensitivity
More than ×1.5 times better detection range
Much lower power consumption for small form outdoor use, with alternate and renewable power supply options
Key Benefits
3D Tracking sensor
© Analog Devices, Inc. 2018, all rights reserved.
Intelligent Traffic Light Radar Sensor
See brochure: “Enabling Smart Traffic
With Advanced Traffic Control Systems”
Play video: “DemoRad_TrafficMonitoring2.avi”

## Slide 17: Use case: Surveillance & Security Monitoring Motion detection and tracking of objects to optimize Surveillance & Security Systems
24 GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLLs) with FMCW ramp generator
  ADAR7251/AD8285 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Multi channel system for digital beam forming:
  Wider field of view
  Best angular resolution
  Multi object or person detection & tracking
Higher receiver system SNR than current available solutions
  3 dB better receiver noise figure
  Improved high performance transmitter phase noise, output power and high speed FMCW ramping
Technical Solution
More than ×2 times improvement in sensitivity
More than ×1.5 times better detection range
Much lower power consumption for small form outdoor use, with alternate and renewable power supply options
Key Benefits
Motion & Tracking Sensor
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 18: Use case: Surveillance & Security Monitoring Motion detection and tracking of objects to optimize Surveillance & Security Systems
24 GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLLs) with FMCW ramp generator
  ADAR7251/AD8285 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Multi channel system for digital beam forming:
  Wider field of view
  Best angular resolution
  Multi object or person detection & tracking
Higher receiver system SNR than current available solutions
  3dB better receiver noise figure
  Improved high performance transmitter phase noise, output power and high speed FMCW ramping
Technical Solution
More than ×2 times improvement in sensitivity
More than ×1.5 times better detection range
Much lower power consumption for small form outdoor use, with alternate and renewable power supply options
Key Benefits
Motion & Tracking Sensor : Radar Plus Camera
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 19: Use case: Unmanned Aerial Vehicle Automatic Collision Avoidance Systems Enabling safer and more autonomous aerial navigation
Full RADAR signal chain solution including the DSP and baseband solution
24 GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLL) with FMCW ramp generation
  ADAR7251/AD8285 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Multi channel system for digital beam forming:
  Wider field of view
  Best angular resolution
  Multi object detection and tracking
Independent low noise transmit and receive functions for spatial flexibility
integrated RF power detectors to enable self test diagnostics
Integrated temperature sensor to reduce components and temperature calibration
Technical Solution
×2 times improvement in sensitivity for object detection
×1.5 times better detection range, to increase speed of autofocus UAV navigation
Lower power consumption reduces UAV payload and battery needs
Key Benefits
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 20: Use case: Radio Altimeters on Unmanned Aerial Vehicles Automating detection of ground or crops tops for optimum low flight operation during inspections or crop spraying
24 GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLL) with FMCW ramp generation
  ADAR7251/AD8285 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Higher receiver system SNR than present available solutions
  3 dB better noise figure
  Improved high performance phase noise, output power and high speed ramping
Independent transmit and receive functions for spatial flexibility
integrated RF power detectors to enable self test diagnostics
Integrated temperature sensor to reduce components and temperature calibration
Technical Solution
24 GHz over traditional 4.3 GHz improves range, accuracy and reduces size
4 times the number of channels increases field of view and angle resolution
Separate Tx and Rx allows for for spatial distribution of antenna elements
Fewer components leading to simpler design, and quicker time to market
Easier development with complete signal chain solution from single supplier
Key Benefits
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 21: Use case: Automotive ACAS Radar Safety Auto safety features – collision avoidance - blind spot detection, lane change assist, cross traffic alert
24 GHz ISM Multi channel FMCW Radar
  ADF5901 (2 Transmit Channels) + ADF5904 (4 Receive Channels)
  ADF4158/9 (FMCW PLLs) with FMCW ramp generator
  ADAR7251/AD8285 4-channel low/high speed 12/14bit-ADC Signal conditioning
  ADSP-BF70X Digital signal processor
Multi channel system for digital beam forming:
  Wider field of view
  Best angular resolution
  Multi vehicle detection
Higher receiver system SNR than current available solutions
  3 dB better receiver noise figure
  Improved high performance transmitter phase noise, output power and high speed FMCW ramping
Technical Solution
More than ×2 times improvement in sensitivity
More than ×1.5 times better detection range
Much lower power consumption for small form factor
Key Benefits
ADAS Radar sensor
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 22: Use case: Aviation Wingtip Radar for Collision Avoidance while Grounded/During Taxiing
Repurpose automotive radar to provide detection for buildings, other aircraft wings and on tarmac vehicles
Flexibility with antennas and small mounting size allows from integration into lighting package
Technical Solution
Proven existing technology
Low costs and flexible design
Lower power consumption allows for use when engines are off
Key Benefits
Aircraft wingtips are subjected to taxi incidents that can be extremely expensive especially with the addition of Winglets
Many accidents happen when aircraft are being moved by a tug
Wing walkers are not specifically trained in taxi and pushback procedures (they are usually baggage handlers)
Challenge
©2018 Analog Devices, Inc. All rights reserved.
Notes: Colission avoidance.

## Slide 23: Analog Devices 24 GHz FMCW Radar Market Summary of Broad Market Applications
Intelligent Traffic Light Monitors
Industrial Tank Level Sensor
Automotive Radar
Radio Altimeter
Collision Avoidance System
Motion - Surveillance & Security
Technical Solution
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 24
©2018 Analog Devices, Inc. All rights reserved.
Radar Technology
24 GHz Radar System Solution Details

## Slide 25: Analog Devices 24 GHz Radar Sensor Platform “DEMORAD” Application Development on a Reference Design - Available on SAP for Purchase
ADF5904 RX
ADF5901 TX
ADF4159 PLL
ADAR7251 AFE
ADSP-BF706
Single Board
©2018 Analog Devices, Inc. All rights reserved.
4RX2TX (MIMO) Radar + ADI-BF-DSP digital baseband + plus basic Radar software & GUI
Radar macros in DSP library
(USB Interface to PC)

## Slide 26: Analog Devices 24 GHz Radar Sensor Platform “DemoRAD” Application Development on a Reference Design
DemoRAD is a standalone radar system with a 24 GHz MIMO FMCW frontend featuring two transmit (TX), four receive (RX) channels, ADC, and a Blackfin DSP from Analog Devices. The system is mainly designed for range-Doppler and MIMO radar applications and the DSP enables real-time signal processing capabilities. The antenna arrangement is chosen to support a uniform virtual array with a spacing of half the wavelength. When using both TX antennas 7 virtual elements can be generated with two virtual element overlapping in order to implement motion compensation algorithms. The main features of the 24 GHz radar system include
  24 GHz ISM band operation
  Sampling rate up to 1.2 MSPS per IF channel
  Ramp Synchronous sampling
  Freely programmable FMCW timing
  MIMO processing with arbitrary antenna activation
  Real-time signal processing on the Blackfin DSP
  USB 2.0 interface for communication.
©2018 Analog Devices, Inc. All rights reserved.

## Slide 27: “DemoRAD” Block Diagram System Eval & solution
A Blackfin BF706 DSP is used to control the RF frontend and to process the measured radar signals of the receive channels. An ADF5901 dual-channel transmitter in conjunction with the frequency-synthesizer ADF4159 is used to generate the FMCW transmit signal. The two TX antennas (TX1, TX2) are fed from the ADF5901 transmitter whereas the receive path of the frontend is realized with a ADF5904 quad-channel receiver. An ADAR7251 analog frontend is used to amplify and sample the measured IF signals of the receiver. Thereafter, the signals are processed in the DSP and the results can be accessed with a USB 2.0 interface. The entire board including the power supply is designed on a single PCB with a total size of 100 mm × 100 mm.
©2018 Analog Devices, Inc. All rights reserved.

## Slide 28: PCB Mechanical Data
©2018 Analog Devices, Inc. All rights reserved.

## Slide 29: Antenna Details
Antenna arrangement with virtual antenna positions.
The serial fed patch antennas feature eight elements with an amplitude taper and are fed from the backside of the PCB. The antennas are fabricated on a Rogers 4350 substrate.
©2018 Analog Devices, Inc. All rights reserved.

## Slide 30: RadarBook vs DemoRAD comparison Ramp Sweep Rate and Range vs Beat Frequency
DemoRad (ADAR7251)
RadarBook (AD8283)
HSR
Low – medium speed FMCW ramps
©2018 Analog Devices, Inc. All rights reserved.

## Slide 31: DemoRAD – Basic Radar Algorithms FMCW Mode - Screen Shots
Raw Data Capture
Radar sys data Range Data over time
©2018 Analog Devices, Inc. All rights reserved.

## Slide 32: DemoRAD – Basic Radar Algorithms Range Doppler Mode
Range and velocity of target
©2018 Analog Devices, Inc. All rights reserved.

## Slide 33: DemoRAD – Basic Radar Algorithms Digital Beam Forming Mode – angle position measurement
Distance and angle of target
©2018 Analog Devices, Inc. All rights reserved.

## Slide 34: Analog Devices 24GHz Sensor Solution Roadmap
Discrete solutions
(5, 10, 24, 60, 78 GHz)
Multichannel integrated 24 GHz ISM radar
Single channel fully integrated 24 GHz wideband radar
Multiple design options, high flexibility
One stop shop for all your signal chain needs
Committed to investing for your future success
©2018 Analog Devices, Inc. All rights reserved.

## Slide 35
©2018 Analog Devices, Inc. All rights reserved.
Radar Technology
24 GHz Radar Chipset Product Details

## Slide 36: ADF5904: 4 Channel Receiver Rx MMIC for 24GHz FMCW Radar Applications
Rx channel gain: 22 dB
Integrated baluns for single-ended receiver (Rx) inputs and local oscillator (LO) input
Noise figure of 10 dB
P1dB: −10 dBm
LO input range: −8 dBm to +5 dBm
Rx to IF isolation: 30 dB
RF signal bandwidth: 250 MHz
Rx output impedance: 900 Ω differential
LO input buffer: 24 GHz
RF and LO S11 at 50 Ω: −5 dB
Temperature sensor with analog output: ±5°
Electrostatic discharge (ESD) performance
  Human body model (HBM): 2000 V
  Charged device model (CDM): 500 V
Qualified for automotive applications
-40 ºC to 105 °C operation
Key Specifications
Highest performance and integration level for 24 GHz multichannel receiver in the industry
Lower total cost of ownership for Rx:
  Highly integrated design eliminates the need for discrete
  Small size sensors using 4 channels in single chip
  Lower power consumption
  Ease of adoption and use
Increased reliability using built in test capability
Key Benefits
©2018 Analog Devices, Inc. All rights reserved.

## Slide 37: ADF5904: 4 Ch. 24 GHz Receiver Rx MMIC for 24 GHz FMCW Radar Applications
Block Diagram
Key Features
  Single-ended Rx inputs: S11 < -12 dB
  20 dB Rx Gain (Fixed)
  NF ≤ 10 dB, P1dB = -10 dBm, IIP3 = 0 dBm
  24 GHz LO input range -20 dBm to 0 dBm
  RX to RX isolation 30 dB
  250 MHz Signal Bandwidth
  ±5° C Temp Sensor, SPI & single 3.3 V supply
  Auto Temperature Range (-40 °C to 105 °C)
  Integrated Test monitors
  Small 5 mm × 5 mm 32-lead LFCSP package
  AECQ100 Automotive Qualified
  All 4 Ch - Power Consumption ~500 mW
  30 dB Rx to Rx isolation
RX Noise Figure vs. RF Freq
RX P1dB
Key Benefit
High Performance Low Power 24 GHz Multi-Channel Receiver
The industry’s best combination of low-noise, high linearity and low-power consumption.
“Best combination of 24 GHz performance and integration on the market”
“Industrial Sensor Customer Testimonial”
High level of µwave integration
  enables simpler PCB system design
  ease of use
  faster time to market.
©2018 Analog Devices, Inc. All rights reserved.
Notes: Slide NOTE:
Help the field to keep the messages clean and clear to customers, and add speaker notes for their use. Include at least major bullet points to be used as discussion points with customers during a presentation.

## Slide 38: ADF5901: 2 Channel Transmitter and VCO Tx MMIC for 24 GHz FMCW Radar applications
24 GHz VCO with 2 channel power amplifier output
  24 GHz to 24.25 GHz voltage controlled oscillator (VCO)
  2-channel 24 GHz power amplifier with 8 dBm output
  Single-ended outputs
  2-channel muxed outputs with mute function
  Programmable output power of -5 dB to +8 dB in 1 dB steps
  N divider output (frequency discriminator)
  24 GHz local oscillator (LO) output buffer
  250 MHz signal bandwidth
  VCO Phase noise:
    -85 dBc/Hz @ 100 kHz offset
    -105 dBc/Hz @ 1 MHz offset
Power control detector
Auxiliary 8-bit ADC
±5°C integrated temperature sensor
Programmable SPI interface
Single supply operation at -3.3 V
170 mA current @ 3.3 V: 560 mW @ 100% duty cycle
Operating temperature range of -40 °C to +105 °C
32-lead, 5 mm × 5 mm LFCSP
Key Specifications
© Analog Devices, Inc. 2018, all rights reserved.
Highest performance integration level for 24 GHz multi-ch transmitter in the industry
Low Phase Noise VCO with on-chip auto cal
Lower total cost of ownership for Tx:
  Highly integrated design eliminates the need for discrete
  Small size using 2 channels in single chip
  Lower power consumption
  Ease of adoption and use
Increased reliability using built in test capability
Key Benefits

## Slide 39: ADF4159: Direct Modulation/ Waveform Generating 13 GHz Fractional-N Frequency Synthesizer PLL with ramp function for 24 GHz FMCW Radar applications
Key Specifications
500 MHz – 13 GHz range
25-bit divider modulus
    Sub-1 Hz frequency resolution
110 MHz PFD maximum frequency
Normalized phase noise floor of -224 dBc/Hz
Programmable phase control
2.7 V to 3.45 V analog power supply
1.8 V digital power supply
Programmable charge pump currents
3-wire programmable serial interface
Digital lock detect
FSK and PSK modulation capabilities
Supports fast ramps
Ramp delay, frequency reed back and interrupt functions
Generates highly linear saw tooth and triangular waveforms
Cycle slip reduction for fast lock times
ESD performance: 3000 V HBM, 1000 V CDM
Qualified for automotive applications
24-LFCSP (4mm × 4mm) package
© Analog Devices, Inc. 2018, all rights reserved.

## Slide 40: ADF4158: Direct Modulation/Waveform Generating 6 GHz Fractional-N Frequency Synthesizer for Slow-Sweep Ramps
KEY FEATURES:
500 MHz – 6 GHz Range
25-bit divider modulus
32 MHz PFD maximum frequency
Supports fast Ramps
Normalized PN Floor = -207 dBc/Hz
FSK Modulation up to 32 MHz PFD
Sub-1Hz frequency resolution
FSK and PSK modulation capability
Generates highly linear saw tooth and triangular waveforms
Cycle slip reduction for fast lock times
24-LFCSP (4mm × 4mm)
Key Benefit
6 GHz Frac-N PLL with FMCW Ramping Waveform Generator
©2018 Analog Devices, Inc. All rights reserved.

## Slide 41: FMCW - Frequency Modulated Continuous Wave Radar Principle (simplified, static condition)
ft
fr
fb=ft-fr
FMCW Radar
Distance: D
ft
t
24.05 GHz
td
fb
fDEV
ts
fr
(1) td = 2*D/c
(3) BW = fDEV*tdmax/ts
(4) BW = fDEV*2*Dmax/(c*ts)
(2) D = c*ts*fb/(fs*2)
ft: Transmit Frequency
fr: Receive Frequency
D: Distance
td: Time of flight for D fb: Beat Frequency
fDEV: Sweep Frequency
ts: Sweep Time c: Light Speed Constant
BW: Max AFE Bandwidth
24.25 GHz
©2018 Analog Devices, Inc. All rights reserved.

## Slide 42: LSR vs HSR FMCW Radar
©2018 Analog Devices, Inc. All rights reserved.

## Slide 43: ADIsimPLL: Simulation Tool for FMCW PLL Ramp Support http://www.analog.com/ADIsimPLL

## Slide 44
©2018 Analog Devices, Inc. All rights reserved.
Radar Technology
Radar
AFE-ADC Product Details

## Slide 45: Analog Baseband (AFE-ADC) Solution LNA, AAF and ADC
Analog Baseband (AFE)
LNA+AAF+ADC
HSR High Speed Ramps
AD8283/84/85
12 MHz Input Bandwidth 80 MSPS (all channel) 12-bit, 67 dB SNR 3.5 nV/Hz @ 1 MHz 34 dB PGA 3rd Elliptical AAF programmable
Pipeline Converter 180 nm Advanced CMOS
LSR High Speed Ramps
ADAR7251
1.2 MHz Input Bandwidth 2.4 MSPS per channel 16-bit, 94.5 dB SNR @ 1.2 MSPS 3.8 nV/Hz @ 1 kHz 45 dB PGA Inherent AAF Programmable EQ Build-in-Selftest for FuSa
Continuous-Time Sigma-Delta 180 nm Advanced CMOS
RX ADC Options for High Speed Ramp or Low Speed Ramp Radar systems
©2018 Analog Devices, Inc. All rights reserved.

## Slide 46: ADAR7251 – 4ch Low Speed Ramp AFE Continuous Time Sigma Delta
Low noise: 2.4 nV/√Hz input referred voltage noise at maximum gain setting
Wide input signal bandwidth: 500 kHz at 1.2 MSPS sample rate, 16-bit resolution
Additional sample rates supported: 300 kSPS, 450 kSPS, 600 kSPS, 900 kSPS, and 1.8 MSPS
4 differential simultaneous sampling channels
No active antialiasing filter required
LNA and PGA with 45 dB gain range in 6 dB steps
Selectable equalizer
Flexible data port supports serial or parallel mode
Supports FSK mode for FMCW radar systems
On-chip 1.5 V reference
Internal oscillator/PLL input: 16 MHz to 54 MHz High speed serial data interface
Key Specifications
©2018 Analog Devices, Inc. All rights reserved.

## Slide 47: AD8285 Radar Receive Path AFE: 4-Channel LNA/PGA/AAF with ADC
4-channel LNA, PGA, and AAF
1 direct to ADC channel
Programmable gain amplifier (PGA)
Includes low noise preamplifier (LNA)
Serial peripheral interface (SPI) programmable gain 16 dB to 34 dB in 6 dB steps
Antialiasing filter (AAF)
Programmable third order, low-pass elliptic filter (LPF) from 1.0 MHz to 12.0 MHz
Analog-to-digital converter (ADC)
12 bits of accuracy up to 72 MSPS
Signal-to-noise ratio (SNR): 68.5 dB
Spurious-free dynamic range (SFDR): 68 dB at gain = 16 dB
Low power: 185 mW per channel at 12 bits and 72 MSPS
Low noise: 3.5 nV/√Hz maximum of input referred voltage noise
Key Specifications
©2018 Analog Devices, Inc. All rights reserved.

## Slide 48: AD8283 - RADAR Receive Path AFE: 6-Channel LNA/PGA/AAF with ADC
6-channels (LNA, PGA, and AAF) multiplexed to one ADC
Programmable gain amplifier (PGA)
Includes low noise preamplifier (LNA) <3nV/rtHz @ max gain
Programmable gain 16 dB to 36 dB in 6 dB steps via SPI interface
Antialiasing filter (AAF)
Programmable 3rd order, low-pass elliptic filter (LPF) from 1.0 MHz to 12.0 MHz
Precise ch-to-ch matching
  Gain: +/-0.5dB (-40 to 105°C)
  Phase: +/-2.5° (-40 to 105°C)
Analog-to-digital converter (ADC)
14 bits of accuracy up to 80 MSPS
Signal-to-noise ratio (SNR): 70 dB
Spurious-free dynamic range (SFDR): 75 dB
Parallel 3.3V CMOS Output
Low power: 150 mW per channel
72 Lead LFCSP
-40 °C to 125 °C
Key Specifications
©2018 Analog Devices, Inc. All rights reserved.

## Slide 49: ADA8282 Radar Receive Path AFE: 4-Channel LNA and PGA
4 channels of low noise amplifiers (LNA) followed by programmable gain amplifiers (PGA)
Minimum −3 dB bandwidth of 5 MHz
Typical –3 dB bandwidth of 42.3 MHz
Typical slew rate of 28 V/µs
Differential input and output
Gain of 18 dB to 36 dB in 6 dB steps
Selectable low noise and low power modes
  Input referred noise of 4.5 nV/√Hz at 18.3 mW per channel
  Input referred noise of 3.6 nV/√Hz at 34.8 mW per channel
  Input referred noise of 3.4 nV/√Hz at 54.8 mW per channel
Qualified for automotive applications
Key Specifications
©2018 Analog Devices, Inc. All rights reserved.

## Slide 50: ADSP-BF706 Blackfin DSP Low Power 400 MHz Blackfin+ Embedded Processor with 1 MByte L2 SRAM
Blackfin+ core with up to 400 MHz performance
  - Dual 16-bit or single 32-bit MAC support per cycle
  - 16-bit complex MAC and many other instruction set enhancements
  - Instruction set compatible with previous Blackfin products
On-Chip Memory
  - 136 KB L1 SRAM with multi-parity-bit protection (64 KB instruction, 64 KB data, 8 KB scratchpad)
  - 1 MByte on-chip L2 SRAM with ECC protection
  - 512 KByte On-chip L2 ROM
Key Peripherals include
  - USB2.0 HS OTG
  - 2× CAN2.0B
  - ePPI Video I/O
  - 2× SPORTs (w/I2S)
  - 2× Quad-SPI / 1 × Dual-SPI (w/ Host mode option)
  - I2C
  - 2× UART
  - SD/SDIO/MMC (4-bit)
Security and one-time-programmable memory
  - Crypto hardware accelerators for fast secure boot/IP protection memDMA encryption/decryption for fast run-time security
Low-cost packaging
  - 88-Lead LFCSP (QFN) package (12 mm × 12mm), RoHS compliant
Low system power with < 100 mW at 400 MHz (< 0.25 mW/MHz) at 25°C TJUNCTION
Key Specifications
©2018 Analog Devices, Inc. All rights reserved.

## Slide 51: Industrial & Automotive Radar Product Signal Chain Roadmap
2015
2016
2017
 | Released To Sales
2018
2019
13 GHz FMCW Fast Ramp PLL
2014
 | ADF4118
 | ADF4193
 | ADF4159 13 GHz FMCW Ramping PLL
 | ADF4158 6 GHz FMCW Ramping PLL
6 GHz fast hopping PLL
13.5 GHz FMCW ultra-Fast Ramp PLL
 | ADF4169 13.5 GHz FMCW Ramping PLL
 | AD8283/AD8284 High speed Ramp AFE
6 Ch & 4 Ch 80MSPS ADC
 | ADA8282 High speed AMP AFE
4 Ch VGA-ADC Driver
 | ADAR7251 Low speed Ramp AFE
4 Ch 1.8MSPS ADC
 | ADF5904 24 GHz ISM RX MMIC
4 Ch 24GHz ISM Band RX MMIC
 | ADF5901 24 GHz ISM TX MMIC
2 Ch 24GHz ISM Band TX MMIC
77/79GHz GaAs
 | All products AECQ100 Auto Qualified
RF PLL + FMCW Ramp Generation
RX AFE ADCs
Microwave TX RX MMICs
 | HMC GaAs MMICs 77/79 GHz RX & TX mmwave
Value Drivers:
High RF Integration Levels with
Low Noise High Linearity performance
Low Power Consumption simplifies design and reduces time to market
Better noise and linearity resulting in greater effective range and accuracy
Qualified to AECQ100
© Analog Devices, Inc. 2018, confidential information, all rights reserved.
Notes: Draw on work done for capability roadmap from BSP document
Note that the start of the box on the time axis represents the start of the project (PSD0) and the end of the box is release (PSD3)
There may not be a clear picture of the entire investment in the out years (2018+) but try to indicate total spend at least for FY16, FY17, and FY18 to give a general shape of the investment direction

## Slide 52: Other ADI Sensor Design RF & Microwave Product Options 5 GHz, 10 GHz and 78 GHz sensors
 | 5 GHz | 10 GHz | 60 GHz (Discrete) | 78 GHz (Discrete)
Synthesizer, or | ADF5355 ( 0.05 – 13.6 GHz VCO/Synthesizer) |  |  | 
 | ADF4355 (6.8 GHz PLL/VCO) |  |  | 
VCO | HMC116x (2 – 38 GHz VCO narrowband VCO family) |  | HMC733 (10 – 20 GHz) | 
PLL | HMC703 (8 GHz Frac-N PLL) |  | ADF41020 (18 GHz Int-N PLL) | 
Multipliers | Not needed | Not needed | HMC1105 (40 – 80 GHz Fout) x2 | 
Mixer | HMC8193 (2 – 8.5 GHz IQ) HMC787A (3 – 11 GHz DBL) | HMC8191 (6 – 26.5 GHz IQ) HMC773A (6 – 26.5GHz DBL) | HMC1081 (50 – 75 GHz DBL) | HMC-MDB277 (40 – 80 GHz Fout) x2
Amplifier | HMC788A (DC – 10 GHz) | HMC1082 (5.5 – 18 GHz) | HMC1144 (40 – 70 GHz) HMC-AUH312 (0.5 – 80 GHz) | HMC-AUH320 (71 – 86 GHz)
LNA | HMC1049 (0.3 – 20 GHz) |  | HMC-ALH382 (57 – 65 GHz) | HMC-ALH509 (71 – 86 GHz) HMC-ALH508 (71 – 86 GHz)
Attenuator | HMC424A (DC – 13 GHz) |  |  | 
Switch | HMC1118 (13 GHz SPDT) |  |  | 
©2018 Analog Devices, Inc. All rights reserved.

## Slide 53: Go to Market Plan
Provide Basic Introduction to RADAR
Introduction to 24 GHz RADAR & Emerging Commercial Sensing applications
Produce 24 GHz RADAR Full Signal Chain diagram
  24 GHz Radar Signal chain Product Detail overview
  Product & Application Level Value Proposition Benefits
  Highlight Broad market 24G RADAR application use cases
Marketing & Application Collateral available on ADI product web sites
  Customer Engagement & Next Steps
    EVB Hardware
      Radar Product Eval boards ready to order & available. Details on product WEB sites
      24G System Eval board ready to order & available. Details on product WEB sites
    Product Application Notes
    Product Briefs
    Datasheets
    Product and Application promotion videos
    Radar Signal chain CFTL
    24 GHz RADAR Sensor Eval Kit HW/SW (Sensor eval platform - DemoRAD)
      Demorad Kit ready to order & available. Details on all product WEB sites
    24G Radar Technical articles
Customer Application Support
  EngineerZone Support Community https://ez.analog.com/welcome
  IDH Partnerzone Support
Product book pricing available on Product WEB site







## Slide 54: RF & Microwave Resources www.analog.com/
Visit the web to view:
http://www.analog.com/en/index.html
24 GHz Multi-channel Radar and Sensor Solution
http://www.analog.com/en/education/education-library/videos/4939173758001.html
24 GHz Radar Signal Chain page
http://www.analog.com/en/applications/landing-pages/001/advanced-driver-assistance-systems.html
24 GHz Radar TX & RX product pages
http://www.analog.com/en/products/rf-microwave/integrated-transceivers-transmitters-receivers/microwave-mmwave-tx-rx/adf5901.html#product-discussions
http://www.analog.com/en/products/rf-microwave/integrated-transceivers-transmitters-receivers/microwave-mmwave-tx-rx/adf5904.html
EngineerZone Support Community https://ez.analog.com/welcome
Application Notes
Product Briefs
Datasheets
Evaluation Boards
Product and Application videos
Radar Signal chain CFTL
Radar Sensor Demo platform (Demorad)
©2018 Analog Devices, Inc. All rights reserved.

## Slide 55
31th Jan 2018
©2018 Analog Devices, Inc. All rights reserved.
Radar Technology Competitive Comparison
ADI 24GHz Radar vs Infineon 24GHz Radar

## Slide 56: ADI’s 24G ADF590X Chipset vs Infineon 24GHz Radar Chipset
Feature | AD5901/ADF5904 | BGT24MTR11 | BGT24MTR12 | ADI solution Benefits | 
# Chs | 2T4R | 1T1R | 1T2R | Better angle resolution (2X ) | 
FMCW PLL | Ext FMCW RF PLL (ADF4159) provided No calibration required | no RF PLL provided Ext PLL or open loop calibration required | no PLL provided Ext PLL or open loop calibration required | Offers full RF & baseband signal chain including AFE-ADCs | 
Rx & Tx Inputs outputs | All Single ended RF connections | Single-ended RX Differential TX Needs Ext RF Balun Larger PCB area | Single-ended RX Differential TX Needs Ext RF Balun Larger PCB area | Simple RF connections smaller PCB footprint: no ext RF components | 
Total Power consumption | 187mW per channel | 250mW / channel | 220mW / channel | ADI offer lower power per ch | 
TX FMCW PLL | Best in Class Phase Noise /FMCW RFPLL | No PLL product available | No PLL product available | ADI leader in RF PLL | 
TX VCO Phase Noise@ 100khz | -88dBc/Hz | -80dBc/Hz | -85dBc/Hz | Lower TX Phase Noise, Better sensor range & angle resolution | 

## Slide 57: ADI’s 24G ADF590X Chipset vs Infineon 24GHz Radar Chipset - Cont
 | AD5901/ADF5904 | BGT24MTR11 | BGT24MTR12 | ADI Solution Benefit | 
TX VCO | Automatic On chip VCO self-calibration. Tracks over temp/ time | External VCO calibration required | External VCO calibration required | Simple to use – no external RF ports to tune - Offers better FMCW freq sweep linearity performance for fast ramps configs vs Temp/Time | 
TX/RX Ch scalability | Povides LO port access, therefore offer easy option to increase RX Ch with zero RF ext components | No LO port access. No Tx or Rx Ch scalability Possible | No LO port access. No Rx Ch scalability Possible | Offers easily cascadable RX solution. Provides even higher angle resolution (4X or better) | 
Flexible Power consumption | Provides programmable power down of all individual Ch’s via SPI | Not as Flexibility | Not as Flexible | ADI offers easy & scalable Lower power per ch. | 

## Slide 58: ADI’s 24G ADF590X Chipset vs Infineon 24GHz Radar Chipset
The Infineon family has 3 RF products
  BGT24MTR11 - 1TX 1RX
  BGT24MTR12 - 1TX 2RX
  BGT24MR2 - 2RX
Cons for Infineon Transmitter and Receiver:
Infineon solutions: TX RF outputs have Differential output not single-ended – Therefore:-
  Requires external balun component on PCB (printed or discrete ) and results in further TX signal loss and process variation
  Larger footprint for external PCB balun to interface to antenna
Infineon solution requires external calibration required due to external port tuning .. Means difficult to use & higher cost of ownership
Infineon TX Phase noise is ~3- 6dB poorer than on ADI TX ADF5901
  means ADI solution can achieve better range & angle resolution for sensor
Infineon solution power consumption for 1TX2RX transceiver is similar to ADI’s 2TX 4RX solution
  means ADI solution is approx. 2X lower power consumption per channel
Infineon solutions have no TX or RX channel scalability (for increasing channel count - has no external LO port access
  ADI solution offers easy TX and RX channel scalability.- with external LO port access
Pros for ADI’s ADF590X chipset
ADI TX & RX MMIC’s all have single ended RF inputs and outputs. easy/simple connection to antenna
ADI TX VCO Calibration on ADF5901 is simpler as no external ports to tune. ( ease of use and lower cost of ownership)
  Offers better FMCW freq sweep Linearity performance for very fast ramps concepts
ADI solution is approx. 2X lower power consumption per channel vs Infineon
ADI solution easily scalable for TX or RX Channel count increase – external LO port access for cascade ability (more than 4 CH)
ADI solution has independent power down control on TX or RX channels if less channels are required
©2018 Analog Devices, Inc. All rights reserved.